## Slide 1: Įvadas į robotiką 7. Varikliai
Aistis Raudys ir Vytautas Valaitis
2019

## Slide 6: Kaip viskas juda
DC varikliai
AC varikliai
Stepereiai
Servo
Selenoidai
Enkoderiai
Valdikliai

## Slide 8: DC Motor Learning Objectives
Explain the role of a snubber diode
Describe how PWM controls DC motor speed
Implement a transistor circuit and Arduino program for PWM control of the DC motor
Use a potentiometer as input to a program that controls fan speed

## Slide 9
What is a snubber diode
and why should I care?

## Slide 10: Simplest DC Motor Circuit
Connect the motor to a DC power supply
Switch open
Switch closed

## Slide 11: Current continues after switch is opened
Opening the switch does not immediately stop current in the motor windings.

## Slide 12: Reverse current
Charge build-up can cause damage

## Slide 13: Motor Model
Simple model of a DC motor:
  Windings have inductance and resistance
  Inductor stores electrical energy in the windings
  We need to provide a way to safely dissipate electrical energy when the switch is opened

## Slide 14: Flyback diode or snubber diode
Adding a diode in parallel with the motor provides a path for dissipation of stored energy when the switch is opened

## Slide 15
Pulse-width modulation (PWM)
for DC motor speed control

## Slide 16: Controlling DC Motor Speed
The voltage supplied to a DC motor controls its speed
Arduino cannot supply variable DC output
  Arduino lacks a true analog output
  Use Pulse-width modulation (PWM) to simulate a variable DC supply voltage
  PWM is a common technique for supplying variable power levels to “slow” electrical devices such as resistive loads, LEDs, and DC motors
  Arduino Uno has 6 PWM pins: Digital I/O pins 3, 5, 6, 9,10, and 11

## Slide 17: Arduno Uno has 6 PWM pins
Look for the ~ prefix on the digital pin label, e.g. ~3

## Slide 18: PWM: Pulsed with modulation
PWM simulates DC voltage control for slow loads
The effective voltage is
is called the duty cycle

## Slide 19: Arduino PWM commands
Configure the output pin:
Set the duty cycle
The duty cycle is an 8 bit value:
0 ≤ duty_cycle ≤255
PWM_pin = ... ; // one of 3, 5, 6, 9, 10, 11
void setup() {
pinMode( PWM_pin, OUTPUT);
}
void loop() {
int duty_cycle = 150; // between 0 and 255
analogWrite( PWM_pin, duty_cycle );
}

## Slide 20
Using a transistor to switch the load

## Slide 21: Transistor as the switching device
Each Arduino output channels has a 40 mA limit
The maximum current draw for an Arduino is 200 mA
Use Arduino as the brain
Let another switching element be the brawn

## Slide 22: Use an NPN Transistor as a switch
This device is designed for use as a medium power amplifier and switch requiring collector currents up to 500 mA

## Slide 23: Electronic components in the fan kit
Transistor
Diode
220 Ω or 330 Ω
resistor

## Slide 24: Replace the Switch with a Transistor
A transistor allows on/off control to be automated and it allows switching of more current than an Arduino digital pin can supply.
Pin 9 or another PWM pin drives the transistor base

## Slide 25: Alternative locations for the transistor
Moving the transistor (and any switch) between the power supply and the motor adds a bit of safety by tying the motor to ground when the system is idle

## Slide 26: Diode and transistor orientation

## Slide 27: Arduno Uno has 5 PWM pins
Look for the ~ prefix on the digital pin label, e.g. ~3

## Slide 28: DC Motor Circuit on tiny breadboard

## Slide 29: +5V connections

## Slide 30: PWM signal is connected to transistor base

## Slide 31: Arduino program to spin the DC Motor
// spin_DC_motor.ino Use PWM to control DC motor speed
int motorPin = 3; // Pin 3 has PWM, connected it to the DC motor
void setup() {
pinMode(motorPin, OUTPUT); // Set motor pin to output mode
}
void loop() {
analogWrite(motorPin, 150); // Motor at 150/255 of full speed
delay(1000);
analogWrite(motorPin, 250); // Motor at 250/255 of full speed
delay(1000);
}
Code is in spin_DC_motor.ino

## Slide 32: Sukimosi Pusės

## Slide 33: How H-Bridge works
Off
Forward
Reverse

## Slide 34: How H-Bridge Works
This represents traditional PWM motor control
Note low average current flow

## Slide 35: H-Bridge: Synchronous Rectification
Use switches instead of diodes
Much more efficient, regenerative braking

## Slide 36: H-Bridge Locked-Antiphase
Pro: one line needed for forward/reverse
Con: higher frequencies needed

## Slide 37: H-Bridge Examples
Functional Truth Table |  |  |  | 
IN1 | IN2 | OUT1 | OUT2 | Comments
L | L | L | L | Brake; both low transistors on
L | H | L | H | Forward
H | L | H | L | Reverse
H | H | H | H | Brake; both high transistors on.
L293, L298, MC33886, TLE5206, TPIC0108b, etc
Simple logic: output = input. Some chips have disables to disconnect all outputs. Advance chips output protection.

## Slide 38: H-Bridge Examples
Functional Truth Table (LM18200) |  |  |  |  | 
PWM | DIR | Brake | OUT1 | OUT2 | Comments
H | H | L | H | L | Forward
H | L | L | L | H | Reverse
L | X | L | H | H | High Side BRAKE
H | H | H | L | L | Low Side Brake
H | L | H | L | L | Low Side BRAKE
L | X | H | Z | Z | None
LM18200, TLE5205, TPIC0107b, etc.

## Slide 40: AC motorai
Ten daug visko
Vienfaziai
Trifaziai
Sudėtinga valdyti
  Reikia generuoti sinusoide
Paliksim kitam kartui

## Slide 41: Stepperiai

## Slide 42: Stepper Motors

## Slide 48: Stepper Motor Selection
Permanent Magnet / Variable Reluctance
Unipolar vs. Bipolar
Number of Stacks
Number of Phases
Degrees Per Step
Microstepping
Pull-In/Pull-Out Torque
Detent Torque

## Slide 51
Step 1 | 0 | 0 | 1 | 1
Step 2 | 1 | 0 | 1 | 0
Step 3 | 1 | 1 | 0 | 0
Step 4 | 0 | 1 | 0 | 1
+
CW
CCW
Control sequence to turn a stepper motor

## Slide 53
Servo Motor Detail
+ 5V
Actuator
Reduction gear
Position feedback
Potentiometer
(closed loop system)
Small electric DC motor

## Slide 55: Brushless Motors and Control

## Slide 56: How do Brushless DC Motors Work?
Switch the position of the magnets and coils.
[8]

## Slide 57: Brushless Control
[12]

## Slide 58: Brushless Motors Brushed Motors
Cheap
Easy to use
Requires few wires
Simple control circuitry
Long lifespan
Very high efficiency
Low noise generation
High power to size ratio